## Slide 1: ESP32 Low Power
Here is where your presentation begins

## Slide 2: TABLE OF CONTENTS INTRODUCTION ABOUT ESP32 ESP32 THINGSBOARD ESP32 AS WEARABLE DEVICE ESP32 LOW POWER 01 02 04 05 03

## Slide 3: 01 INTRODUCTION

## Slide 4: LAST YEARS
Link github (https://bit.ly/30RHsZ3) https://github.com/hasbiida/TrainingEspRpi
ESP32 – Cloud/Rpi (dash python+database)
ESP32 simple webserver

## Slide 5: HIGHLIGHTS THIS YEARS ESP32 Thingsboard ESP32 low power 01 02 03 ESP32 as Wearable device
ESP32 as IoT node devices
How to tuning ESP for lower energy usage
How to plot sensor data to smartphone (esp as webserver)

## Slide 6: ABOUT ESP32 02

## Slide 7: GETTING STARTED ESP32 PROGRAMMING ENV SPEC 01 03 02
Arduino IDE
Espressif IDF
Micropython
JavaScript
LUA
A feature-rich MCU with integrated Wi-Fi and
Bluetooth connectivity for a wide-range
of applications
Dual core
Wi-Fi and bluetooth
32 bit programs.
Freq up to 240MHz and it has a 512 kB RAM
30 or 36 pins

## Slide 8: EXAMPLES OF ESP32 BOARDS

## Slide 10: ARDUINO IDE
Install IDE
Add board manager URL
https://dl.espressif.com/dl/package_esp32_index.json
Tools  board  board manager  esp32
Open example blink
change pin 22 (led built in)
Upload

## Slide 11: ESP32 THINGSBOARD 03
ESP32 as IoT node devices

## Slide 12: Download bahan materi https://github.com/hasbiestheim/FGD_Tel-U_2020 https://bit.ly/3iPmUGG

## Slide 13: INSTALL LIBRARY
Thingsboard
ArduinoHttpClient
ArduinoJson
DHT sensor library

## Slide 14: PROGRAM NODE IOT THINGSBOARD
Untuk sensor DHT11
  ESP32_thingsboard_DHT11
Untuk sensor Pulse Sensor
  ESP32_thingsboard_PulseSensor

## Slide 15: THINGS BOARD LOGIN

## Slide 16: THINGSBOARD DASHBOARD
ThingsBoard is an open-source server-side platform yang memungkinkan untuk monitor dan control perangkat IoT. Gratis untuk digunakan secara personal dan commercial dan dapat digunakan dimana saja

## Slide 17: FITUR DARI THINGSBOARD
Provision perangkat, aset, dan pelanggan serta menentukan hubungan di antara mereka.
Kumpulkan dan visualisasikan data dari perangkat dan aset.
Menganalisis telemetri yang masuk dan memicu alarm dengan pemrosesan peristiwa yang kompleks.
Kontrol perangkat Anda menggunakan remote produce call(RPC).
Buat alur kerja berdasarkan life cycle perangkat, event, REST API, RPC request, dll
Desain dasbor dinamis dan responsif serta telemetri perangkat atau aset dan wawasan terkini kepada pelanggan Anda
Aktifkan fitur khusus kasus penggunaan menggunakan rule-chain yang dapat disesuaikan.
Push data perangkat ke sistem lain.
demo.thingsboard.io/

## Slide 18: THINGSBOARD

## Slide 19: KONEKSI ESP DENGAN THINGSBOARD
Add device dan copy access token pada demo.thingsboard.io
Sesuaikan access token dengan device node (esp32)
Cek koneksi pada telemetry
Buat dashboard dengan data sesuai datatelemetry

## Slide 20: INTERNET ALL THE THINGS

## Slide 21: ESP32 AS WEARABLE DEVICE 04
How to plot sensor data to smartphone (esp as webserver)

## Slide 22: PERBEDAAN ESP AS CLIENT ESP AS WEBSERVER

## Slide 23: Install ESP32 Filesystem Uploader in Arduino IDE
Arduino IDE directory, and open the Tools
Copy folder ESP32FS to Tools folder
Restart Arduino IDE

## Slide 24: Plot Sensor Readings in Real Time Charts – Web Server
Install Filesystem uploader plugin
Install Libaries ESPAsyncWebServer and AsyncTCP
Uploading Code and Files - Tools > ESP32/ESP8266 Data Sketch Upload
Web Server using SPIFFS (SPI Flash File System)
Notes: server.on("/style.css", HTTP_GET, [](AsyncWebServerRequest *request){ request->send(SPIFFS, "/style.css","text/css");

## Slide 25: ESP32 LOW POWER 05
How to tuning ESP for lower energy usage

## Slide 26: DESAIN METRIC
METRIC (1- 5) | PRIORITY | ADVANTAGES | DISADVANTAGES
CONNECTIVITY | 3 | Low power | Lambat dan jarak dekat
POWER MANAGEMENT | 5 | Small battery | Low performance
SECURITY | 2 | Low cost | Unsecure
COMPLEXITY | 3 | Mudah digunakan | Terbatas
RAPID EVOLUTION | 1 | Arduino support | Terbatas

## Slide 27: PARAMETER CONNECTIVITY
Range
Throughput
Power source
Topology
Notes: Mau diaplikasikan kemana aja
Seberapa cepat datanya/realtime
Catu daya batrai/selfpowered/grid
Simple start sampai gateway

## Slide 28: ESP32 Power Modes
Active Mode
Modem Sleep Mode
Light Sleep Mode
Deep Sleep Mode
Hibernation Mode

## Slide 29
Notes: What is Clock Gating?
Clock gating is a technique for reducing the dynamic power consumption.
It disables portions of the circuitry by powering off clock pulses, so that the flip-flops in them do not have to switch states. As switching states consumes power, when not being switched, the power consumption goes to zero.

## Slide 30: Code Diff (Thingsboard sleepy) using sleep timer
RTC store data
Init sleep timer (waker)
Function to print cause of wake up
Sleep command in main program
RTC_DATA_ATTR int bootCount = 0;
esp_deep_sleep_start()
void print_wakeup_reason()
esp_sleep_enable_timer_wakeup(time_in_us)

## Slide 31: Code Diff (Chart webserver sleepy) using touch wake up
RTC store data
Init touchpin and threshold sensitivuty (waker)
Function to print cause of wake up
Sleep command in main program
RTC_DATA_ATTR int bootCount = 0;
void print_wakeup_reason()
#define Threshold 40
﻿touchAttachInterrupt(T3, callback, Threshold);
esp_sleep_enable_touchpad_wakeup()﻿

## Slide 32: THANKS
Do you have any questions?
hasbiida@gmail.com
Please keep this slide for attribution